## Slide 1: Internet of Things
Chip McClelland

## Slide 2: Agenda
Problem statement
Selection criteria
Some options considered / explored
GPRS Example – Xively
WiFi Example – data.sparkfun.com
Next Up – Power and Cost optimization

## Slide 3: Problem Statement
There is no shortage of cheap and ubiquitous sensors to collect data.
But…
I need to reduce the time and effort to retrieve that data and
a mechanism to quickly, continuously and automatically share it.

## Slide 4: Communications Options

## Slide 5: Data Service Options
Xively
  Professional Internet of Things Site
  Easy and free to get started
  Integrated graphing – great documentation
  Commercial service – not cheap
Data.Sparkfun.com
  Based on open-source Phant – roll your own
  Less integrated – access via .CSV and .JSON only
  Public by default – unclear commercial future

## Slide 6: GPRS & Xively
Pros:
  Simplified design: location, time, storage
  Works just about anywhere
  Range of communication choices: Http, JSON, SMS
  Bi-directional / ubiquitous
Cons:
  Power consumption – up to 500mA when sending
  Speed – GPRS service only
  Can’t do SSL due to Arduino limitations
  Cost - $2/day or $60/month
  Communicate using SoftwareSerial AT commands - painful

## Slide 7: CC3000 & Sparkfun
Pros:
  Simplified design: location, time, storage
  WiFi broadly available
  Range of communication choices: Http, JSON, SMS
  Speed / Bandwidth
  Communicates using SPI Bus- Buy the Adafruit version!
Cons:
  Does not work with “Captive Portal” networks!
  Can’t do SSL due to Arduino limitations
  Bi-directional possible but need something like DynDNS

## Slide 8: Next Up
Like most embedded projects – Power and Price
Power Optimization
  New power supply for both
  Sleep and software control of modem
  LiPoly batteries
Price
  Custom board
  Less expensive data services – Adafruit exploring?