## Slide 1: My Home Automation
Paul MacDougal
TriEmbed.org
August 10, 2020

## Slide 2: My Layout
Ubiquity
Edgerouter
WiFi
AP
Raspberry Pi
Zero WiFi
ESP8266
based
devices
Amazon
DASH
buttons
192.168.2.x
subnet
Cable
Modem
Internet

## Slide 3: Edgerouter
https://www.ui.com/edgemax/edgerouter-poe/
1 million packets per second
24V/48V Passive PoE (not currently in use)
5 ports configured like this:
  WAN
  192.168.2.x subnet
  192.168.0.x subnet
  192.168.0.x subnet
  192.168.0.x subnet

## Slide 4: DHCP
Edgerouter handles DHCP for all devices. Static mapping set for each device based on MAC address.

## Slide 5: DNS
Edgerouter runs local DNS (dnsmasq) to allow accessing devices by name rather than IP address.
Amazon DASH button desires access to dash-button-na.amazon.com
Local /etc/hosts file spoofs IP address of dash-button-na.amazon.com to IP address of Raspberry Pi Zero. (Thanks Huan Truong)

## Slide 6: Wireless MAC filtering
The AP does MAC filtering on all devices.
Requires knowing the MAC address of each allowed device and editing the AP settings before connection is allowed.

## Slide 7: MQTT
Raspberry Pi Zero W runs MQTT broker
  sudo apt-get install mosquitto
  sudo apt-get install mosquitto-clients

## Slide 8: Smart Plugs
Sonoff S31 ($18 15A energy monitoring)
Gosund WP3 ($6 10A)
Reflashed with Tasmota firmware

## Slide 9: Tasmota
Open source firmware for ESP8266 based devices.
The M in Tasmota stands for MQTT
Devices publish telemetry and subscribe to command topics

## Slide 10: Washer monitor
Sonoff S31 device flashed with Tasmota

## Slide 11: Washer monitor (cont)
pubs to MQTT topic: tele/sonoffE/SENSOR
{ "Time":"2020-06-28T18:59:45", "ENERGY":{ …, "Voltage":121, "Current":0.049 } }

## Slide 12: Python script on Pi
Subscribes to local MQTT broker topic: "tele/#"
Publishes select values to Adafruit
def on_message(client, userdata, msg):
. . .
elif u'tele/sonoffE/SENSOR' == msg.topic:
data = json.loads(msg.payload)
publishAdafruit('h.w', data['ENERGY']['Current'])
publishAdafruit('h.wv', data['ENERGY']['Voltage'])

## Slide 13: io.adafruit.com
Notes: Mosquitto does not retain topic messages, so we send them on to io.adafruit.com, which keeps around 30 days (60 for paid account) worth of data.

## Slide 14: Smart Washer
So far, we just log the data. I want to know when the cycle has finished. Need a monitor of some sort.
D1 mini subscribes to local MQTT broker topic: "tele/sonoffE/SENSOR"
Looks for the drop at the end of the final spin and beeps the buzzer.

## Slide 15: Status Device

## Slide 16: Status Display
Garage Door closed
Irrigation Off
Laser Off
Washer Idle Off
Time

## Slide 17: Garage Monitor
D1 mini Lite with custom shield for Dallas one-wire devices.
Notes: D1 mini Lite has ESP8285 with 1M Flash internal to the processor chip.

## Slide 18: Garage Monitor (cont)
Temperature probes inside and outside of garage
Switch on door.

## Slide 19: Garage Monitor
Publishes a JSON message to MQTT topic: tele/<device id>/SENSOR
{ "Sketch":"esp_garage_door_temp v1.2", "T0":824, "T1":932, "SQ":-59, "door":0, "doorCount":1555, }
Notes: SQ is RSSI (Received Signal Strength Indicator) of WiFi connection
Door count is saved in EEPROM. It is the number of rising/falling edges seen on the door switch (debounced).

## Slide 20: Garage Data
Notes: This is a dashboard from io.adafruit.com

## Slide 21: Soil Probe
D1 mini Pro w/ Lipo battery
Awakens from deep sleep, measures A0 voltage, and sends data

## Slide 22: Time is energy
Using standard WiFi connection takes around 6-7 seconds to publish MQTT topic.
ESP-NOW is a vendor specific protocol that can send data in less than 0.5 sec of awake time.

## Slide 23: Soil Probe (cont)
ESP-NOW monitor running on D1 mini receives packet from soil probe.
Uses softwareSerial to communicate with another D1 mini Lite which publishes the data to MQTT
ESP-NOW
WiFi
Notes: ESP8266 can run in either ESP-NOW or WiFi mode.
This unit is USB powered with a wall wart.

## Slide 24: Gemini Board
Connect two D1 mini boards
14  16, 16  14
3v3  3v3, gnd  gnd

## Slide 25: Soil Probe summary
D1 mini Pro sends data via ESP-NOW
D1 mini receives ESP-NOW and sends it via serial to D1 mini Lite
D1 mini Lite publishes to MQTT on Pi
Python on Pi subscribes to the topic and sends the data to io.adafruit.com

## Slide 26: Soil Probe Data
Notes: I haven’t quite figured this out yet. I think the sharp up spikes are rain/watering events.

## Slide 27: Soil Probe Battery
No data
No data
Notes: Low reading 2020/08/06 9:00:21pm 382
Low reading 2020/08/07 2:09:04am 382
Last reading 2020/08/07 6:16:08am 384
Recharge 2020/08/09 6:40:56pm 371

## Slide 28: Don’t you plug in your plants?
Notes: Charging the battery in the soil probe.
Need to react to the battery voltage getting low.

## Slide 29: How reliable is it?
Notes: Here, we see the Sonoff S31 reported voltage over a month.
I don’t see any data outages. This means the Tasmota firmware and the Pi software are running well.
This daily variation of line voltage is interesting.

## Slide 30: Reliability (cont)
No data
Notes: My custom code is not doing as well. Sometimes things stop working for unknown reasons.
I need to detect when they stop sending data. I expect data from most devices every 15 seconds.

## Slide 31: To be continued …